Changes in ACPI 3.0
(slides from Intel Developer Forum Fall '04 ACPI 3. 0 class by Guy Therien – hacked by Len Brown)
Class targeted System vendors and BIOS writers
Original presentation at http://www.acpi.info

---
ACPI 3.0 Overview
Summary
Configuration support for: PCI Express*, Serial ATA, Intel® High Definition Audio, Multi-core / Multi-threaded Processor Power Mgt., Enhanced Device Hot Plug, NUMA Distancing, >256 Processors, Ambient Light Sensor Device, Battery Recalibration
Extended Thermal Model / Thermal requirements tightened
Notification of OS Capabilities and Control Negotiation
Improved Robustness: device description, wake source, device-centric enhancements, wake / sleep / wake sequencing, display extensions
*Other names and brands may be claimed as the property of others.

---
Agenda
Agenda
Operating System Support
General Configuration Enhancements
New Interconnect Support
Inter-Processor Dependency Support
New Devices and Device Specific Enhancements
Thermal Control Enhancements
Server Related Enhancements
Wake / Sleep Enhancements
ASL Grammar Enhancements and Clarifications

---
Operating System Support Summary
Operating System Support Summary
ACPI 3.0 Operating System support will be evolutional
Seek guidance from OS Vendors for specific ACPI 3.0 feature support timelines

---
Terms and Symbols
Terms and Symbols
OSPM: OS-directed Configuration and Power Management – any system software (driver or core OS) that manipulates ACPI-defined interfaces
Lower Importance: OSPM development may be needed
Important: Required in certain cases
Very Important: Required / Potential Near-Term OS Focus

---
General Configuration Enhancements
General Configuration Enhancements
_OSI (Operating System Interfaces)
_PDC (Processor Driver Capabilities)
_OSC (Operating System Capabilities)
_DSM (Device Specific Method)
_PLD (Port Location Description)
_MLS (Multi-language string)
Extended Address Space Descriptor
New FADT flags
NVRAM support
General Purpose Event Clarification

---
_OSI (Operating System Interfaces)
_OSI (Operating System Interfaces)
Platform query of supported OSPM interfaces, behaviors, and features
Commonly evaluated in \_SB.INI
Boolean evaluation of a string parameter
  - Strings are OS vendor or ACPI defined
Allows OSPM to convey multi OS support
OSPM may expose new functionality based on string arguments
General Configuration Enhancements

---
General Configuration Enhancements - _OSI
Scope (_SB) {	//Scope
 Name (TOOS, 0)	// Global variable for type of OS.
 // This methods sets the "TOOS" variable depending on the type of OS
 // installed on the system.
 // TOOS = 1	// Windows 98 & SE
 // TOOS = 2	// Windows Me.
 // TOOS = 3	// Windows 2000 OS or above version.
 // TOOS = 4	// Windows XP OS or above version.
 Method (_INI) {
  If (CondRefOf (_OSI,Local0)) {
   If (\_OSI ("Windows 2001"))
      { Store(4, TOOS) }
   }
   Else {
    Store (\_OS, local0)
     If (LEqual (local0, "Microsoft Windows NT"))
     { Store (3, TOOS) }
     ElseIf (LEqual (Local0, "Microsoft Windows"))
     { Store (1, TOOS) }
     ElseIf (LEqual (Local0, "Microsoft WindowsME:Millennium Edition"))
     { Store (2, TOOS) }
    }
 } //_INI Method
} //_SB scope

---
General Configuration Enhancements - _OSI Conditional Table Load
Scope (_SB) {
 Method (_INI) {
  If (CondRefOf (_OSI,Local0)) {
   If (\_OSI ("Module Device")) {
     LoadTable(“OEM1", “OEMID", “Table1",,,)}
   Else
     {LoadTable(“OEM1", “OEMID", “Table2",,,)}
  }
  Else
   {LoadTable(“OEM1", “OEMID", “Table2",,,)}
 } //_INI Method
} //_SB scope
DefinitionBlock (“MD1SSDT.aml",“OEM1",0x02,
       “OEMID", "Table1", 0) {
Scope(\_SB) {
 Device (\_SB.NOD0) {
   Name (_HID, "ACPI0004") // Module device
   Name (_UID, 0)
   Name (_PRS, ResourceTemplate() { ... })
   Method (_SRS, 1) { ... }
   Method (_CRS, 0) { ... }
   Device (PCI0) { // PCI Root Bridge
     Name (_HID, EISAID("PNP0A03"))
     Name (_UID, 0)
     Name (_BBN, 0x00)
     Name (_PRS, ResourceTemplate () {...})
    } // end of PCI Root Bridge
  } // end of Module device
 } // end of \_SB Scope
} // end of Definition Block
DefinitionBlock (“MD1SSDT.aml",“OEM1",0x02,
       “OEMID", "Table2", 0) {
 Scope(\_SB) {
  Device (PCI0) { // PCI Root Bridge
   Name (_HID, EISAID("PNP0A03"))
   Name (_UID, 0)
   Name (_BBN, 0x00)
   Name (_PRS, ResourceTemplate () {...})
  } // end of PCI Root Bridge
 } // end of \_SB Scope
} // end of Definition Block

---
_PDC (Processor Driver Capabilities)
_PDC (Processor Driver Capabilities)
Conveys OSPM processor driver support capabilities to the platform
Provides means for OSPM to assume native control of a processor related function
Evaluated before other processor power / performance management objects
  - Return values from other objects may change based upon OSPM capabilities
Capabilities bit definitions specified by CPU vendor
  - (http://developer.intel.com/technology/iapc/acpi/downloads/302223.htm)
Replaced by _OSC (next slide)
General Configuration Enhancements

---
_OSC (Operating System Capabilities)
_OSC (Operating System Capabilities)
Conveys OSPM capabilities at the device level
Provides means for OSPM to assume and release native control of a platform function
Evaluated before other device objects
  - Return values from other objects may change based upon OSPM capabilities
Enables compatible ID device superset functionality
Platform Notification may trigger re-evaluation
Among first users are PCI Express, CM Battery, and Processor driver (replaces _PDC)
General Configuration Enhancements

---
_DSM (Device Specific Method)
_DSM (Device Specific Method)
Generic control method device object
Eliminates potential object name collision for compatible ID devices
Control method operation is selected by arguments:
  - UUID
  - Revision ID
  - Function Index
  - Additional arguments
General Configuration Enhancements

---
_PLD (Physical Location Description)
_PLD (Physical Location Description)
Describes a device’s external connection
Descriptions include:
  - Visibility
  - Surface where the connector is located
  - Position
  - Grouping
  - Color
  - Width
  - Height
  - Bay
  - Ejectability
  - Cabinet
  - Card Cage
  - OEM-specific extended data
Platform can notify OSPM when location changes
General Configuration Enhancements

---
_MLS (Multiple Language String)
_MLS (Multiple Language String)
Provides OSPM with a human-readable device description in multiple languages
Typically used for diagnostic purposes
Expands on _STR functionality
Evaluates to packages of language identifiers and Unicode strings
  - Language ID String: RFC 3066
  - Unicode (UTF-16) encoding
General Configuration Enhancements

---
Extended Address Space Descriptor
Extended Address Space Descriptor
Allows platform to describe additional memory attributes
Compliments EFI GetMemoryMap() in the case of dynamic reconfiguration
  - Adds cacheability attributes
Supports QWORD addressing
OSPM support indicated via _OSI feature group string
  - “Extended Address Space Descriptor”
General Configuration Enhancements

---
New FADT Fixed Feature Flags
New FADT Fixed Feature Flags
USE_PLATFORM_CLOCK
  - Set when platform contains correct ACPI PM Timer implementation
S4_RTC_STS_VALID
  - Set when contents of RTC_STS is correct on S4 exit
REMOTE_POWER_ON_CAPABLE
  - Set if platform supports leaving GPE wake events enabled when entering S5
General Configuration Enhancements

---
NVRAM Support
NVRAM Support
Worn out NVRAM should be listed in memory map as AddressRangeReserved
INT 15H, E820H - Query System Address Map, Address Range Descriptor Extended Attributes – bit 1
  - set if address range is non volatile
Extended Address Space Descriptor, Type Specific Attributes field
  - ACPI_MEMORY_NV 0x0000000000008000
OSPM must characterize NVRAM for use suitability
General Configuration Enhancements

---
General Purpose Event Clarification
General Purpose Event Clarification
Only the power, lid, and sleep buttons GPEs can be both runtime and wake GPEs
All other GPEs must be either runtime or wake GPEs - Not both
General Configuration Enhancements

---
New Interconnect Support
New Interconnect Support
PCI Express*
Serial ATA
Intel® High Definition Audio
*Other names and brands may be claimed as the property of others.

---
PCI Express*
PCI Express*
PCI Express features require ACPI-based configuration support
Memory mapped configuration space
  - MCFG Data Table provides boot time base address
  - _CBA (Configuration Base Address) object provides base address for hot plugged root bridges
  - Need to disable memory OpRegion ASL access to configuration space when OS supports PCI Express natively
_OSC and PCI Express
  - Native Hot Plug enable / disable
  - Native Power Management enable / disable)
  - Required for a host bridge device that originates a PCI Express hierarchy
  - Optional for a host bridge device that originates a PCI / PCI-X bus hierarchy
See PCI Firmware Specification Revision 3.0 for more information (http://www.pcisig.com)
  - New PNP0A08 hardware identifier (_HID) – PCI Express host bridge
New Interconnect Support
*Other names and brands may be claimed as the property of others.

---
Serial ATA
Serial ATA
_ADR support
  - ATA Port: High word - Root port #, Low word - port number off of a SATA port multiplier, or 0xFFFF if no port multiplier attached
_SDD (Set Device Data)
  - Conveys device type to platform
  - Used to create task file data returned by _GTF
  - Replaces _GTM and _STM for SATA
_GTF
  - Evaluated after _SDD
Supported by Intel® Application Accelerator 4.5
New Interconnect Support

---
Intel® High Definition Audio
Intel® High Definition Audio
_ADR
  - High word – SDI (Serial Data In) ID of the codec that contains the function group
  - Low word – Node ID of the function group
ACPI configuration object specification document currently under development
  - Pin Configuration
  - OEM Customization
  - Array Microphone support
  - See http://developer.intel.com for information as it becomes available
New Interconnect Support

---
Inter-Processor Dependency Support
Inter-Processor Dependency Support
Processor Execution Resources
AS
APIC
AS
APIC
Vcc
GHI#
STPCLK# (C2)
DPSLP# (C3)
P-state controls
C2 / C3
C-state controls
Logical processors share the physical package & P/C state controls
When one processor enters C2 / C3, both enter that state
Causes problems if non-idle processor is servicing interrupts
When one processor transitions to a P-state, both will transition
Potentially non-optimal behavior if one processor idle and the other busy
OSPM must coordinate to ensure correct & optimal operation
P0
P1
Multi-processor, multi-threaded processor, and multi-cored processor platforms have inter-processor dependencies
Power states, throttling states, performance states
Example Dependency: Multi-threaded processor with 2 threads
[Speaker Notes: George to update]

---
Inter-Processor Dependency Support – Cont.
Inter-Processor Dependency Support – Cont.
New processor objects convey inter-processor dependencies to OSPM
  - _CSD (C-state Dependency)
  - _TSD (T-state Dependency)
  - _PSD (P-state Dependency)
Dependent processors are declared as members of a “dependency domain”
Platform conveys existence of HW coordination or need for SW coordination to OSPM
C-state dependency conveyed on a per state level
  - Example: Dependency may exist for C3 but not for C1
_OSC / _PDC conveys OSPM support to the platform

---
Inter-Processor Dependency Support
Processor (
\_SB.CPU0,	// Processor Name
1,	// ACPI Processor number
0x120,	// PBlk system IO address
6 )	// PBlkLen
{Name (_CST, Package()
 { 3, // There are three C-states defined here with three semantics
 Package(){ResourceTemplate(){Register(FFixedHW, 0, 0, 0)}, 1, 20, 1000},
 Package(){ResourceTemplate(){Register(SystemIO, 8, 0, 0x161)}, 2, 40, 750},
 Package(){ResourceTemplate(){Register(SystemIO, 8, 0, 0x162)}, 3, 60, 500}
})
Name(_CSD, Package()
{ Package(){6, 0, 0, 0xFD, 2, 1},	// 6 entries, Revision 0, Domain 0, OSPM Coordinate
// Initiate on Any Proc, 2 Procs, Index 1 (C2-type)
  Package(){6, 0, 0, 0xFD, 2, 2}	// 6 entries, Revision 0, Domain 0, OSPM Coordinate
// Initiate on Any Proc, 2 Procs, Index 2 (C3-type)
}) }
Processor (
\_SB.CPU1,	// Processor Name
2,	// ACPI Processor number
,	// PBlk system IO address
)	// PBlkLen
{ Name(_CST, Package()
{ 3,	// There are three C-states defined here with three semantics
  Package(){ResourceTemplate(){Register(FFixedHW, 0, 0, 0)}, 1, 20, 1000},
  Package(){ResourceTemplate(){Register(SystemIO, 8, 0, 0x161)}, 2, 40, 750},
  Package(){ResourceTemplate(){Register(SystemIO, 8, 0, 0x162)}, 3, 60, 500}
})
Name(_CSD, Package()
{ Package(){6, 0, 0, 0xFD, 2, 1},	// 6 entries, Revision 0, Domain 0, OSPM Coordinate
// Initiate on any Proc, 2 Procs, Index 1 (C2-type)
  Package(){6, 0, 0, 0xFD, 2, 2}	// 6 entries, Revision 0, Domain 0, OSPM Coordinate
// Initiate on any Proc, 2 Procs, Index 2 (C3-type)
})}

---
New Devices and Device Specific Enhancements
New Devices and Device Specific Enhancements
Ambient Light Sensor Device
User Presence Detection Device
USB Port Configuration
Battery Related Enhancements
Display Extension Enhancements

---
Ambient Light Sensor Device
Ambient Light Sensor Device
Control Method device that reports Ambient Light information
Potential uses include adjusting display brightness in proportion to ambient light
_ALI (Ambient Light Illuminance)
_ALC (Ambient Light Color Chromacity)
_ALT (Ambient Light Temperature)
_ALR (Ambient Light Response)
_ALP (Ambient Light Polling)
Platform issues notifies upon meaningful changes in Ambient Light information
New Devices and Device Specific Enhancements

---
User Presence Detection Device
User Presence Detection Device
Control Method device that reports user’s presence
Potential uses include powering down display when user is not present
_UPD (User Presence Detect)
  - Evaluates to indicator of user’s presence
_UPP (User Presence Polling)
  - Evaluates to recommended sensor polling frequency
Platform notifies OSPM to re-evaluate _UPD when a change in user presence occurs
New Devices and Device Specific Enhancements

---
USB Port Configuration
USB Port Configuration
_UPC (USB Port Capabilities) object conveys platform specific port attributes to OSPM
  - Connectibility – can a user connect a USB device to the port?
  - Connector Type
    - 0x00:	Type ‘A’ connector
    - 0x01:	Mini-AB connector
    - 0x02:	ExpressCard
    - 0x03 - 0xFE:	Reserved
    - 0xFF:	Proprietary connector
New Devices and Device Specific Enhancements

---
Battery Related Enhancements
Battery Related Enhancements
_BTM (Battery Time)
  - Evaluates to estimated run time at current rate of discharge or given a specified rate of discharge
_BLT (Battery Level Threshold)
  - \_SI object conveys user’s preference for warning, low, and wake levels
Battery Recalibration Support
  - Recovers battery capacity
  - OS-based recalibration replaces firmware or custom application based recalibration
  - _BMD (Battery Maintenance Data)
    - Returns Capabilities and Status
  - _BMC (Battery Maintenance Control)
    - Calibration control, charger control, discharge while A/C connected control
New Devices and Device Specific Enhancements

---
Display Extension Enhancements
Display Extension Enhancements
_DOD (Enumerate Display Devices)
  - Device IDs now clearly defined by:
    - Display Index, Display Port Attachment, and Display Type
    - Bit 31 set to indicate conformity to new scheme
_BQC (Brightness Query Current Level)
New Display Device Notifications
  - 0x82 – Cycle Display Output Hotkey Pressed
  - 0x83 – Next Display Output Hotkey Pressed
  - 0x84 – Previous Display Output Hotkey Pressed
  - 0x85 – Cycle Brightness
  - 0x86 – Increase Brightness
  - 0x87 – Decrease Brightness
  - 0x88 – Zero Brightness
  - 0x89 – Display Device Off
New Devices and Device Specific Enhancements

---
Thermal Control Enhancements
Thermal Control Enhancements
Requirements Clarification
New Throttling Control Objects
Extended Thermal Model
Other New Thermal Objects

---
Requirements Clarification
Requirements Clarification
To achieve optimal performance, quality of service, and adherence to user preferences, non OSPM-based thermal management is prohibited
Exceptions:
  - Failsafe thermal control
  - Platforms containing only Active thermal controls
Designs guides will require compliance
Thermal Control Enhancements

---
New Throttling Control Objects
New Throttling Control Objects
Similar to performance state control objects
_PTC (Processor Throttling Control)
  - Defines throttling control and status registers
_TSS (Throttling Supported States)
  - Table of throttling states and control / status values
_TPC (Throttling Present Capabilities)
  - Specifies the number of currently available throttling states
  - Platform notification signals re-evaluation
Do not use performance state control objects (_PCT, _PSS, _PPC) to perform linear throttling
Thermal Control Enhancements

---
ACPI Thermal Model Assumptions
ACPI Thermal Model Assumptions
The original ACPI thermal model made certain assumptions including:
  - Thermal sensors and programmable trip points are accessible from ASL
  - Processors are the only generators of significant thermal load
  - Only processors have Passive cooling controls
Thermal Control Enhancements – Extended Thermal Model

---
The New Thermal Environment
The New Thermal Environment
Future platforms will contain multiple devices that:
  - Are significant generators of thermal load
  - Contain embedded thermal sensors and programmable trip points
  - Contain embedded Passive and Active thermal controls
  - Are thermally sensitive
    - While not being significant thermal load generators themselves
  - Are co-located such that the thermal load generated by one device may adversely impact a nearby device
  - Share Active cooling devices (fans)
Thermal Control Enhancements – Extended Thermal Model

---
Extended Thermal Model
Extended Thermal Model
Extends ACPI thermal zone to support multiple devices within a single thermal zone
Device components may contain embedded temperature sensors, programmable trip points, and cooling controls (Active and Passive)
Thermal interfaces exposed via device’s driver
Thermal relationships between devices are expressed by means of a thermal relationship table
OSPM support detected using _OSI
  - “3.0 Thermal Model”
Thermal Control Enhancements – Extended Thermal Model

---
Extended Thermal Model – Thermal Zone
Extended Thermal Model – Thermal Zone
Thermal Control Enhancements – Extended Thermal Model

---
New Thermal Objects
New Thermal Objects
_TRT (Thermal Relationship Table)
  - Conveys interaction between devices to OSPM
_TPT (Trip Point Temperature)
  - Allows platform to implement hysteresis
_TST (Temperature Sensor Threshold)
  - Conveys programmable trip point separation
  - Enables elimination of Passive policy polling
_TZM (Thermal Zone Member)
  - Associates a device with a thermal zone
Thermal objects can now exist under devices
  - _PSV, _HOT, _CRT, _ACx, _SCP, etc.
Thermal Control Enhancements – Extended Thermal Model

---
Other New Thermal Objects
Other New Thermal Objects
_SCP (Set Cooling Policy)
  - Acoustic and power limit arguments added
  - Enables platform to place Passive trip point among multiple Active trip points
_RTV (Relative Temperature Values)
  - Conveys to OSPM that temperature values are relative values as opposed to absolute values
  - Temperature values are relative to (below) maximum value of the critical trip point
Thermal Control Enhancements

---
Server Related Enhancements
Server Related Enhancements
Large System Support
NUMA Enhancements
Hot Plug Enhancements
VGA Presence

---
Large System Support
Large System Support
Systems with more than 256 processors now supported
Processors may now be declared as a “Device”
  - New ACPI0007 hardware identifier (_HID)
Linkage to Local SAPIC ID/EID accomplished using match between
  - Device _UID (Unique Identifier) field and
  - New fields in MADT Processor Local SAPIC Structure
    - ACPI Processor UID Value
    - ACPI Processor UID String
Server Related Enhancements

---
NUMA Enhancements
NUMA Enhancements
System Resource Affinity Table (SRAT)
  - Provides boot time association of processors and memory ranges to a System Locality / Proximity Domain
System Locality Information Table (SLIT)
  - Provides boot time description of relative distances between all System Localities / Proximity Domains
  - Matrix – distance may change with direction
_SLI (System Locality Information)
  - Provides runtime update of SLIT
Server Related Enhancements

---
Hot Plug Enhancements
Hot Plug Enhancements
_OST (OSPM Status Indication)
  - Enables OSPM / Platform handshaking during device ejection, hot add, or other event processing
  - Source events include both Notifies and OS initiated events
_GSB (Global System Interrupt Base)
  - Enables Hot Plug of I/O APICs
  - Used to process corresponding _MAT entries
Server Related Enhancements

---
_HPX (Hot Plug Parameter Extensions)
_HPX (Hot Plug Parameter Extensions)
Provides device configuration parameters for a static or hot plugged PCI device
Adds PCI-X configuration data
  - Maximum memory read byte count
  - Average maximum outstanding split transactions
  - Total maximum outstanding split transactions
Adds PCI Express* configuration data
  - Advanced Error Reporting Extended Capability Structure programming
Supersedes _HPP (Hot Plug Parameters)
Server Related Enhancements – Hot Plug Enhancements
*Other names and brands may be claimed as the property of others.

---
VGA Presence
VGA Presence
New FADT Boot Architecture Flags bit - VGA Not Present
If set inhibits OSPM blind probe the VGA hardware (that responds to MMIO addresses A0000h-BFFFFh and IO ports 3B0h-3BBh and 3C0h-3DFh)
  - Eliminates potential machine check exception
Server Related Enhancements

---
Wake / Sleep Enhancements
Wake / Sleep Enhancements
_SWS (System Wake Source)
_SxW (Sx Device Wake State)
_DSW (Device Sleep Wake)
_TTS (Transition To State)

---
_SWS (System Wake Source)
_SWS (System Wake Source)
Enables OSPM to definitively determine cause for platform transition to S0 state
May exist under \_GPE, \_SB, or GPE Block Device scopes
Platform must take care to preserve the wake event source
Source event must be valid for all transitions into S0 state and be persistent while in S0 state
Wake / Sleep Enhancements

---
_SxW (Sx Device Wake State)
_SxW (Sx Device Wake State)
Enables OSPM to place device in lowest power D-state where device wake is possible given a target system sleeping state (S-state)
_SxD provides highest possible power D-state in an S-state
  - If wake is supported from an S-state then device CAN wake the system from D-state returned by _SXD
Wake / Sleep Enhancements

---
_DSW (Device Sleep Wake)
_DSW (Device Sleep Wake)
Expands capability of _PSW
Provides platform with System S-state and Device D-state that will exist when wake capability should be enabled
  - Value range governed by _SxD and _SxW
Allows device / platform to comprehend device wake while system is in S0 state
Wake / Sleep Enhancements

---
_TTS (Transition To State)
_TTS (Transition To State)
New control method OSPM executes during Wake / Sleep / Wake process
Provides platform with next S-state
  - S0, S1, S2, S3, S4, S5
During Sleep, evaluated before device driver notification
During Wake, evaluated after device driver notification
Abort of sleeping state transition will result in _TTS evaluation indicating S0
Wake / Sleep Enhancements

---
Wake / Sleep Enhancements
Working / Sleeping State Object Evaluation Flow

---
ASL Grammar Enhancements and Clarifications
ASL Grammar Enhancements and Clarifications
Timer (Get 64-bit Timer Value)
  - returns a monotonically increasing value (100ns units)
Function (Declare Control Method)
  - Explicit declaration of a control method that returns a result
  - Enables better compile-time error checking
ToUUID (Convert String to UUID Buffer Macro)
  - “aabbccdd-eeff-gghh-iijj-kkllmmnnoopp”
New resource descriptor macros
  - ExtendedIO, ExtendedMemory, ExtendedSpace

---
ASL Clarifications – Cont.
ASL Clarifications – Cont.
Logical operators
  - Buffer and string support clarified - not just integers
  - Implicit conversion is supported - first operand determines type
Method calling convention
  - New section clarifies convention and behaviors of ArgX, LocalX and global variables
  - New section explicitly defines ArgX, LocalX and Named variable behavior – “Rules for Reading and Writing Objects”
ASL grammar section divided into sub-sections, for clarity:
  - ASL Name and Pathname terms
  - ASL Root and Secondary terms
  - ASL Data and Constant terms
  - ASL Opcode terms
  - ASL Primary (Terminal) terms (alphabetical)
  - ASL Parameter and Keyword terms
  - ASL Resource Template terms
ASL Language section restructured:
  - ASL Operator Summary (new)
  - ASL Operator Summary By Type (new)
  - ASL Operator Reference –
    - completely alphabetical
    - Includes Syntax, Arguments, Description for each operator

---
Next Steps
Next Steps
Download the ACPI 3.0 Specification
Become an ACPI 3.0 Specification adopter
Devices vendors – Develop ACPI-compatible Ambient Light Sensor and User Presence Detection devices
Seek guidance from software suppliers on OS and driver support timelines
Please send us specification errata and clarification requests
http://www.acpi.info